Nanometer-Scale Structure and Properties of Dilute Semiconductor Alloys

Rachel S. Goldman

Department of Materials Science and Engineering

University of Michigan

For many compound semiconductors, the addition of dilute concentrations of impurities leads to dramatic changes in the electronic, optical, and magnetic properties.  For example, the introduction of a few percent nitrogen into GaAs leads to a band gap reduction of 100s of meV. Furthermore,  the incorporation of a few percent manganese into GaAs enables a combination of semiconducting and ferromagnetic behavior.  The resulting narrow gap nitride and dilute magnetic semiconductors are promising for several applications ranging from long-wavelength light-emitters and high efficiency solar cells to spin-electronics and spin-optoelectronics.  In both cases, the nanometer-scale details of impurity incorporation are critical to understanding and controlling the observed properties.  In this talk, I will discuss our recent investigations of the growth, nanometer-scale structure, and properties of dilute GaAsN and GaMnAs alloys, using nuclear reaction analysis (NRA) and cross-sectional scanning tunneling microscopy (XSTM), in conjunction with several other measurements.   In the case of GaAsN, I will discuss the incorporation of nitrogen into substitutional vs. interstitial lattice sites, and its effect on electronic and optical properties.  In the case of GaMnAs, I will discuss clustering of MnGa and AsGa point defects, and its effect on electronic and magnetic properties.

This work is supported in part by the Department of Energy, through the National Renewable Energy Laboratory Photovoltaics Beyond the Horizon Program, the National Science Foundation (NSF), the Air Force Office of Scientific Research, the Office of Naval Research, the TRW Foundation, and NASA-Lewis.

Biography:

Rachel S. Goldman is an Associate Professor of Materials Science and Engineering at the University of Michigan.  She received her B.S. degree in Physics (High Honors with Distinction) from the University of Michigan in 1988, her M.S. degree in Applied Physics from Cornell University in 1992, and her PhD in Materials Science from the University of California, San Diego in 1995. In 1994, Goldman received the MRS Graduate Student Award.  Following her PhD, she was a postdoctoral fellow at Carnegie Mellon University from 1995 to 1996.  In 1997, she joined U-M as the Dow Corning Assistant Professor. Goldman’s research interests are in the atomic-scale design of electronic materials, with a focus on the mechanisms of strain relaxation, alloy formation, and diffusion; and correlations between microstructure and electronic, magnetic, and optical properties of semiconductor films, nanostructures, and heterostructures. She received a National Science Foundation CAREER Award in 1998, a Career Development Award from U-M in 1999, a Poster Award from the Materials Research Society in 2000, and the Peter Mark Memorial Award from the American Vacuum Society in 2002.