DCC registers:

DCC software Switch: (address 0x07)

Bit9=’1’ & Bit0=’0’, enable the switch, which is bit[8:1], corresponding to the binary hardware switch bit[8:1].

Bit12=’1’ & bit15=’0’, Disable the TTC ready.  Not to use the TTC fiber input, so the TTC command can be set by VME simulation;

Bit13=’1’ & bit14=’0’, Ignore the SLINK_Full backpressure;

Bit14=’1’ & bit13=’0’, Ignore the SLINK_Down and SLINK_Full backpressure.

L1A generation: (address 0x04)

Bit[15:8]=delay[7:0]: delay between L1As

Bit[7:0]: number of L1As to be sent, minimum number is 1, even Bit[7:0]=0;

Status High (address 0x02)

Status low (address 0x01)

Bit[15:0]: number of L1As received by DCC;(see also address 0x09 for high order)

Bit16=’0’: SLINK0: full, = ‘1’, not full (SLINK backpressure)

Bit17=’0’: SLINK0: down, = ‘1’, powered up (SLINK power down);

Bit18=’0’: SLINK1: full, = ‘1’, not full (SLINK backpressure)

Bit19=’0’: SLINK1: down, = ‘1’, powered up (SLINK power down);

Bit[22:20]: IN_FIFO Half_Full (the upper three IN_FPGA related FIFOs);

Bit[27:23]: IN_FIFO Almost_Full (Two In-FIFO per bit, per In_FPGA)

Bit[31:28]: sTTS status; (changed in version 22 to match FMM definitions)

|  | Hex Value |
| --- | --- |
| FMM State | < ver 22 | >= ver 22 |
| Ready | 0x2 | 0x8 |
| Warning | 0x4 | 0x1 |
| Out-of-Sync | 0x8 | 0x2 |
| Busy | 0x1 | 0x4 |
| Error | 0x3 | 0xC |
| Disconnect | 0x0 or 0xF | 0x0 or 0xF |

TTC VME register (address 0x00)

Bit0: Event number counter reset;

Bit1: BeamCrossing counter reset;

Bit[7:2]: TTC command bus TC[5:0].

FMM test register (address 0x08)

| Bit: | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | x | SLINK B | SLINK A | sTTS |
|  | x | E | R | B | O | W | E | R | B | O | W | E | R | B | O | W |

Where:

E = Enable (Force state)

R = Ready

B = Busy

O = Out-of-Sync

W = Warning

L1A Count High Order Byte: (address 0x09)

Bit[15:8] = 0

Bit[7:0] = L1A count bits [23:16]

Input Fifo Status: (address 0x0A)

(Two FIFO flags OR’ed per bit, one for each FPGA)

Bit[15:10] = 0

Bit[9:5] = IN_FIFO Almost_Full  (same as Status[27:23])

Bit[4:0] = IN_FIFO Half_Full  ([2:0] are same as Status[22:20])