Transformer (5K30.20)

Location: 4-2R

Concept/Purpose: Transformers

Procedure/Explanation: A simple transformer constructed of two identical solenoids and an incandescent light bulb. The first solenoid (primary) is wired to 120 AC line voltage while the second (secondary) is wired to the light bulb. The secondary rests on top of the primary and can easily be removed and replaced. With the current on in the primary and the secondary removed the bulb does not glow. The secondary is then placed on the primary and the bulb glows. To increase the bulb’s intensity even more, a large iron core can be lowered into the center of the solenoids.