Flick The Card (1F20.34)

Location: 15-4L

Concept/Purpose: Inertia of Rest

Procedure/Explanation: This device consists of a small platform with a metal post mounted at its center. An index card is placed on the post with a steel ball directly above the post on top of the card. About two inches from the post is a thin piece of stiff metal.  Pull this back and the recoil strikes the edge of the index card sending it off at a high enough speed that the inertia of the ball allows it to remain sitting on top of the post.