Siren Disk (3C20.30)

Location: Q-1C

Concept/Purpose: Various frequency sound waves.

Procedure/Explanation: The siren disk is a circular metal disk with a series of holes drilled through it at various radii. The disk is mounted to a motor and oriented vertically in front of an air supply nozzle. The motor rotates the wheel at a constant rpm resulting in a single frequency sound wave. Different frequencies are produced by moving the air nozzle to the next series of holes at a different radius.