Capacitor and Fan (5C30.32)

Location: 8-4R

Concept/Purpose: Energy Stored in a Capacitor

Procedure/Explanation: A 1 Farad (2.5 Volt) capacitor is charged up for about 5-10 seconds with a 3 Volt battery pack.  The capacitor is then disconnected from the battery and connected to a small motor with a fan blade.  The motor runs for a few seconds showing that the capacitor is discharging current. A 10 Farad (2.5 Volt) capacitor is also available to run the fan and compare the amount of time it runs to the time of the 1 Farad capacitor.