Fuse Board (5F20.33)

Location: Dick

Concept/Purpose:  Circuit Analysis

Procedure/Explanation: The demo consists of five light bulbs wired in parallel and a small wire acting as a fuse in series with the light bulbs. The circuit is connected to a 12V power supply.  Each bulb has its own switch so they can be turned on one by one. As each bulb is turned on the total resistance in the circuit decreases resulting in an increase in current. When the fourth or fifth bulb is turned on the current becomes high enough to burn out the fuse wire.