Magnetic Field: Wire (5H15.10)

Location: 29-5L

Concept/Purpose: Fields and Currents

Procedure/Explanation: A metal bolt is inserted into a Plexiglas sheet, with wires attached to each end of the bolt.  The Plexiglas sheet is placed on the overhead so that the bolt is seen head on.  Iron filings are sprinkled around the bolt and a large current is then passed through the wires using a 12-volt battery. The iron filings will gather along the magnetic field lines to reveal their shapes around the wire.