Spinning Magnet with Tap Switch (5K40.23)

Location: 4-1C

Concept/Purpose: Motors and Generators

Procedure/Explanation: A small iron core solenoid is connected to a 6 Volt battery and a tap switch. A few inches from the end of the solenoid is a small plastic pivot holding a bar magnet, allowing the magnet to rotate in the horizontal plane. Using the tap switch the solenoid is turned on and off to make the magnet spin. It takes a little practice to get the timing just right to keep the magnet spinning.